## Slide 1: Ibex VP with a Daemon-Based NPU
How a QEMU TCG plugin connects an Ibex virtual platform to a matrix-multiply accelerator running in its own process
Branch ibex-matmul-daemon · October 2026
VP
QEMU + TCG plugin
Unix socket
NPU
matmul_daemon
Notes: This deck explains what we built and how. The virtual platform (VP) is QEMU's ibexdemo machine running Ibex RISC-V firmware with TCG, QEMU's fast instruction translator. The NPU is a matrix-multiply accelerator that runs as a separate host process, matmul_daemon. A QEMU TCG plugin connects the two over a Unix socket. Sections: architecture, how each piece was built, how it was validated (GDB, performance, tests, two platforms), and lessons and next steps.

## Slide 2: What we built
A separate NPU process
matmul_daemon computes C = A × B for any number of VPs over a Unix socket.
0
QEMU source patches
Connected by a QEMU TCG plugin
The plugin turns the doorbell write into a socket request. No QEMU source changes.
22
automated tests, GDB included
Deterministic and tested
The guest waits for every result; failures become error codes, never hangs.
2
platforms, identical results
Notes: Three ideas carry the whole project. First, the accelerator (we call it the NPU) is its own operating-system process, so it can be developed, replaced, restarted, or shared without touching QEMU. Second, the connection is a QEMU TCG plugin: QEMU loads it with -plugin, and it uses only the public plugin API, so QEMU's source is unchanged; the only requirement is QEMU built with --enable-plugins. Third, the guest waits at the doorbell until the result is in memory, so every run is deterministic; and every failure (no daemon, a crashed daemon, a slow daemon, a bad request) becomes an error code the firmware can read rather than a hang. The right column: zero QEMU patches, 22 automated tests including a real GDB session, and identical results on macOS and Linux.

## Slide 3: Where we started
Oct 16
e4307ca
QEMU runs the CPU; GPIO in Verilator
Oct 22
a3ac4c1
Whole SoC in Verilator; QEMU is the console
Oct 22
f938bb0
QEMU CPU with RTL GPIO, UART, timer
Oct 23
9de0957
Plugin computes the GEMM inside QEMU
Oct 28
21267e2–acc7191
This work: the NPU in its own daemon
Step 4's idea, the math done inside QEMU, survives as the “direct” build that the performance slides compare against.
Notes: The repository grew in steps. October 16: QEMU emulated the CPU and forwarded GPIO accesses to a Verilator RTL model. October 22: the whole Ibex SoC moved into Verilator, with QEMU only stepping it and acting as the UART console; the same day a mode with QEMU's CPU plus RTL GPIO, UART and timer was added. October 23: the first TCG plugin appeared, but it computed the matrix multiply inside the QEMU process. This work, October 28, moved the matrix multiply into its own daemon process and made the plugin a thin client. The old in-QEMU approach lives on as a 'direct' build of the same plugin, compiled with -DMATMUL_PLUGIN_DIRECT, used only as the performance baseline.

## Slide 4: Architecture
01
Two processes, one socket, two contracts
Notes: This section covers the structure: which processes exist, how they talk, and the two interfaces (contracts) that keep the pieces independent.

## Slide 5: Two processes, one socket
QEMU process · the VP
matmul_daemon · the NPU
vCPU thread: Ibex firmware
Runs RISC-V code with TCG; stores 1 to 0x0011C014
matmul_plugin.so
Store callback reads A and B, sends the request, writes C and STATUS
Main thread
poll() on the socket; accepts each VP and starts a thread for it
Client thread, one per VP
Checks the request, runs C = A × B, replies with C and timing
Unix socket
GEMM: n, A, B
C + timing
Socket /tmp/ibex-matmul-accel.sock, owner-only (mode 0600). One daemon can serve many VPs at once.
Notes: Left: the QEMU process. Its vCPU thread runs the Ibex firmware through TCG. The plugin lives inside the same process and runs on that vCPU thread whenever the firmware stores to the doorbell address. Right: the daemon process. Its main thread waits in poll() for new connections and starts one thread per connected VP; each client thread reads requests, validates them, computes C = A × B, and replies. Between them is a Unix stream socket, /tmp/ibex-matmul-accel.sock by default, created owner-only so other users on the machine can't send it work. The request carries n, A and B; the reply carries C plus the multiply-accumulate count and how long the math took.

## Slide 6: Three components, two contracts
Firmware
sw/matmul_accel/main.c
Fills A and B, rings the doorbell, checks C
Plugin
matmul_plugin.c
Spots the doorbell and moves the data
Daemon
matmul_daemon.c
Checks requests, runs the GEMM, replies
Guest mailbox
matmul_accel.h
Seven words of guest RAM
Wire protocol
matmul_daemon_protocol.h
16-byte header + payload
The guest never sees the socket. The daemon never sees guest addresses.
Notes: There are three components and two contracts between them. The firmware and the plugin agree on the guest mailbox, defined in tcg_plugin/matmul_accel.h: seven 32-bit words in guest RAM. The plugin and the daemon agree on the wire protocol, defined in include/matmul_daemon_protocol.h: a 16-byte header followed by a payload. Because the contracts are separate, the firmware knows nothing about sockets, and the daemon only ever sees matrices, never guest addresses. That separation is what makes the daemon replaceable, for example by an RTL model of an NPU, without changing the firmware or the plugin. Sizes: firmware 157 lines, plugin 510, daemon 680; the GEMM kernel itself is a 26-line shared header.

## Slide 7: Life of one request
1
Write N, A, B, C,
then store to KICK
2
Callback reads
the mailbox, A, B
3
Send GEMM
with n, A, B
4
Check it, then
compute C = A × B
5
Reply with C
(GEMM_DONE)
6
Write C, then
STATUS = DONE
7
Resumes, sees
DONE, uses C
Firmware (guest)
Plugin (in QEMU)
Daemon (NPU)
The firmware stays paused at the KICK store until step 6, so the result is always ready.
Notes: One request, step by step. 1: the firmware writes the matrix size N and the addresses of A, B and C into the mailbox, clears STATUS, and stores 1 to KICK at 0x0011C014. 2: that store triggers the plugin's memory callback on the vCPU thread; the plugin reads the mailbox and copies A and B out of guest memory. 3: it sends a GEMM message with n, A and B. 4: a daemon client thread validates the request and computes C = A × B. 5: it replies with GEMM_DONE carrying C and timing. 6: the plugin writes C into guest memory, then ERRCODE and STATUS. 7: only now does the firmware execute its next instruction, which reads STATUS = DONE. Because steps 2-6 happen inside the store, the result is always ready and the run is deterministic.

## Slide 8: How it was built
02
Mailbox, plugin, protocol, daemon, scripts
Notes: This section walks through each piece in the order a request touches it: the guest mailbox, the plugin, the wire protocol, the daemon, and the scripts that build and run everything.

## Slide 9: The guest mailbox
Address | Register | Meaning
0x0011C000 | N | matrix size, 1–32
0x0011C004 | A | address of matrix A
0x0011C008 | B | address of matrix B
0x0011C00C | C | address for result C
0x0011C010 | STATUS | 0 idle · 1 done · 2 error
0x0011C014 | KICK | any store starts a request
0x0011C018 | ERRCODE | why it failed
Firmware must end below 0x0011C000. Without the plugin, a bounded poll reports “no response” instead of hanging.
ERRCODE values
1 bad N (0 or above 32)
2 guest memory error
3 daemon down or too slow
4 daemon rejected it
Why not a device?
Plugins can watch memory but can't add devices, so a RAM mailbox needs no QEMU patch.
Notes: The firmware talks to the NPU through seven 32-bit words at 0x0011C000, in ordinary guest RAM just below the stack. The firmware writes N and the three matrix addresses, sets STATUS to 0, then stores anything to KICK. The plugin answers by setting STATUS to 1 (done) or 2 (error), with ERRCODE saying why: 1 for a bad N, 2 if guest memory couldn't be read or written, 3 if the daemon is unreachable or didn't answer within the timeout, 4 if the daemon rejected the request. Why RAM instead of a proper MMIO device? A QEMU plugin can observe execution and memory accesses, but it can't add devices to the machine; a device would need a QEMU patch. The trade-off: without the plugin loaded, the writes just land in RAM, so the firmware polls STATUS a bounded number of times and reports 'no response' rather than hanging. The firmware also checks at startup that its own data ends below the mailbox.

## Slide 10: The plugin: store to request
TRANSLATION TIME
vcpu_tb_trans() adds a store callback to every guest instruction
EVERY STORE
vcpu_mem_cb() ignores all stores except one to 0x0011C014
THE DOORBELL
handle_kick() reads the mailbox, A and B, calls transact(), writes C and STATUS
Robustness rules
Fails fast: QEMU won't start without a daemon
Every send and reply has a deadline (timeout_ms)
Non-blocking socket: macOS ignores MSG_DONTWAIT
SIGPIPE off: a dead daemon is an error, not a crash
Retries once on a new connection; a GEMM is idempotent
Notes: How the plugin finds the doorbell. When QEMU translates a block of guest code, it calls the plugin's vcpu_tb_trans(), which registers a store-only memory callback on every instruction. At run time vcpu_mem_cb() runs for every guest store and returns immediately unless the address is KICK. On the doorbell, handle_kick() reads the mailbox and the A and B matrices from guest memory, sends one request with transact(), and writes C, ERRCODE and STATUS back. Robustness rules: the plugin connects and says HELLO when it loads, and refuses to load if no daemon answers, so problems show up before the guest starts. Every send and every reply wait is bounded by timeout_ms (default 5000 ms). The socket is non-blocking, because a 32x32 request is bigger than macOS's 8 KiB socket buffer and macOS ignores MSG_DONTWAIT on Unix stream sockets. SIGPIPE is suppressed so a dead daemon returns an error instead of killing QEMU. After a transport failure it reconnects once and resends, which is safe because a GEMM has no side effects.

## Slide 11: The wire protocol
magic
u32 · “IMMD”
version
u16 · 1
type
u16
seq
u32 · echoed
len
u32 · payload bytes
0
4
6
8
12
16
16-byte header, then len payload bytes. Little-endian; struct sizes pinned with _Static_assert.
Message | Direction | Payload
HELLO (1) | plugin → daemon | client PID
HELLO_ACK (2) | daemon → plugin | PID, max N, served
GEMM (3) | plugin → daemon | n, flags, A, B
GEMM_DONE (4) | daemon → plugin | n, MACs, ns, C
ERROR (5) | daemon → plugin | code, detail
Two kinds of errors
Keep the connection
Bad N or unknown type: reply ERROR, keep reading
Close the connection
Bad magic, version, or length: the stream can't be trusted
Notes: Every message starts with the same 16-byte header: a magic number (the bytes 'IMMD'), a protocol version (1), a message type, a sequence number that the reply echoes, and the payload length. Then come len payload bytes. All fields are little-endian, and _Static_assert checks pin every struct's size so a compiler or padding change can't silently break the format. Five message types: HELLO and HELLO_ACK at connect time (the daemon reports its PID, the largest N it accepts, and how many GEMMs it has served), GEMM and GEMM_DONE for the work itself, and ERROR. Errors come in two kinds: if the request is well-formed but wrong (bad N, unknown type) the daemon replies ERROR and keeps the connection; if the framing is wrong (bad magic, version or length) it replies ERROR and closes, because the next byte can't be trusted to start a header.

## Slide 12: The daemon: a careful service
1 · Detach
Double fork and setsid. The parent exits only once the socket is ready.
2 · Claim the socket
Refuses a live daemon, replaces a stale socket, never deletes other files. Mode 0600.
3 · Signal ready
Logs to a file, writes the pidfile, then tells the parent it's ready.
4 · Serve
poll() on the socket and a wake-up pipe; one thread per connected VP.
5 · Stop cleanly
SIGTERM wakes poll(); it removes the socket and pidfile only if they're its own.
Built-in client: --ping prints its PID and GEMMs served; matmul_daemon.sh relies on it.
Notes: The daemon behaves like a proper Unix service. 1, Detach: with --daemon it forks, calls setsid, and forks again; the original process waits on a pipe and exits successfully only when the grandchild reports that the socket is listening, so whoever started it can connect immediately. 2, Claim the socket: if something already answers on the path it refuses to start; if the file is a stale socket left by a crash it replaces it; if the path is a regular file it refuses rather than delete it. The socket is created with umask 077, so only your user can connect. 3, Signal ready: only after binding does it send its output to the log file and write the pidfile; that way startup errors still reach your terminal. 4, Serve: the main thread polls the listening socket and a wake-up pipe, and each connection gets its own thread; a mutex protects only the shared counters. 5, Stop cleanly: SIGTERM, SIGINT or SIGHUP write a byte to the wake-up pipe; the main loop exits and removes the socket and pidfile, but only if the socket's inode and the pidfile's PID still belong to this process.

## Slide 13: Build and run scripts
build_matmul_plugin.sh
Turns on QEMU plugin support once, keeping existing options, builds QEMU incrementally, then runs make.
Makefile
Builds the daemon, both plugin variants, and the firmware. Probes GCC for its RISC-V ISA naming.
matmul_daemon.sh
start, stop, restart, status, log, foreground. stop asks the daemon itself for its PID.
run_matmul_plugin.sh
Reuses or starts a daemon, runs QEMU, shows the daemon log, cleans up. --gdb pauses for a debugger.
Notes: Four files make it easy to build and run. build_matmul_plugin.sh checks whether QEMU was configured with plugin support; if not, it re-runs QEMU's configure through config.status with --enable-plugins added, which keeps every other option. It then runs an incremental QEMU build (a no-op when up to date) and make. The Makefile builds the daemon, both plugin variants, and the firmware; because RISC-V toolchains differ by age, it test-compiles once to see whether GCC wants the newer rv32imc_zicsr_zifencei name or plain rv32imc. matmul_daemon.sh manages the background daemon; stop asks the daemon for its own PID over the socket, so a stale pidfile can never make it signal an unrelated process. run_matmul_plugin.sh is the one-command demo: it reuses a running daemon or starts one, runs QEMU with a watchdog, prints the daemon's log for the run, and stops the daemon only if it started it. Options: --gdb, KEEP_DAEMON=1, QEMU_TIMEOUT, IBEX_MATMUL_SOCKET.

## Slide 14: Validation
03
GDB, performance, tests, two platforms
Notes: This section shows the evidence: a real GDB session, measured performance against the direct (in-QEMU) build, the automated tests, and identical results on macOS and Linux.

## Slide 15: GDB works unchanged
1
Terminal A
run_matmul_plugin.sh --gdb
VP paused, GDB server on port 1234
2
Terminal B
riscv32-unknown-elf-gdb
attached to the firmware ELF
3
Then
break, step, read memory as usual;
the daemon just waits
One stepi over the doorbell store moves STATUS from 0 to 1, with C already in memory.
(gdb) target remote :1234
(gdb) break kick
(gdb) continue
Breakpoint 1, kick (n=4)
(gdb) p/x *(unsigned*)0x0011C010
$1 = 0x0
(gdb) finish
Value returned is $2 = 1
(gdb) p/x *(unsigned*)0x0011C010
$3 = 0x1
(gdb) p c[0]@4
$4 = {-7852, -7334, 5318, -27399}
Notes: QEMU's built-in GDB server is independent of TCG plugins, so debugging works exactly as without the NPU. run_matmul_plugin.sh --gdb starts QEMU paused with -gdb tcp::1234 -S and turns off the launcher's 60-second watchdog. In a second terminal you attach riscv32-unknown-elf-gdb (or gdb-multiarch) to build/matmul_accel.elf. The session on the right is abridged from a real run: break in kick(), check STATUS is 0, run kick() to its return with finish, which sends the request through the daemon, and STATUS is now 1 and the first results are in C. Single-stepping one instruction over the doorbell store shows the same thing: the whole round trip completes inside that store. While the VP sits at a breakpoint, the daemon simply waits. An automated test drives this exact session.

## Slide 16: I/O performance: no change
Chart: seconds per run
| No plugin | Direct (in QEMU) | Daemon NPU
Time per run | 2.034 | 2.075 | 2.119
+2–4%
for both plugins, vs no plugin
Which plugin comes out ahead flips from run to run, so the gap between them is noise.
Workload: 2 s of firmware computation and UART output, no NPU requests. Median of 7 runs on an Apple M3 Pro.
Notes: Question: does attaching the NPU slow down the rest of the guest, its computation and its I/O? The benchmark firmware runs about two seconds of software matrix math and UART printing without ever ringing the doorbell. Without a plugin it takes 2.034 s; with the direct plugin 2.075 s; with the daemon plugin 2.119 s. Both plugins cost 2-4% because both watch every guest store; the order between the two plugins flips from run to run, so they are the same within noise. The daemon adds nothing to ordinary guest execution. Reproduce with python3 ibex-vp-cosim/scripts/bench_npu.py.

## Slide 17: Per request: direct is faster
Chart: µs per request
| 4×4 | 8×8 | 16×16 | 32×32
Direct (in QEMU) | 3 | 3 | 3.5 | 6.3
Daemon NPU | 14.1 | 14.2 | 16 | 27
Average per request · 2,000 per size · median of 7 runs
+11–21 µs
extra per daemon request
Why
Process switches and data copies; the VP waits each time.
When the daemon pays off
Heavy or RTL NPU models, shared NPUs, crash isolation.
To beat direct
Asynchronous requests: the guest runs while the NPU computes.
Notes: Per request, the direct build is faster: 3.0 to 6.3 µs against 14.1 to 27.0 µs for the daemon, so the daemon adds 11 to 21 µs per request. The math is the same in both (one shared kernel). The extra time is the round trip: the request crosses into another process and back, which costs two context switches and copying A, B and C (up to 12 KiB at 32x32). Because the VP waits for each request, nothing hides that cost. So a daemon is not a speed win for synchronous small GEMMs. It pays off when the NPU model is heavy or separate (for example a Verilator RTL NPU), when several VPs share one NPU, or when an NPU crash must not take down QEMU. To beat the direct build on speed, requests would need to be asynchronous, so the guest keeps running while the NPU computes on another core. That mode is not implemented yet.

## Slide 18: 22 tests in about 5 seconds
22
automated tests
The hung-daemon test found a real freeze; see “Problems found and fixed”.
5
Lifecycle
detach, pidfile, cleanup, stale sockets
6
Protocol
N = 1–64 vs a reference, every error
1
Parallel
six VPs on one daemon
3
End to end
PASS, no daemon, no plugin
2
Recovery
daemon restart, hung daemon
2
Baseline
direct matches daemon; timing log
1
GDB
a real debug session
2
Scripts
launcher and control script
Notes: python3 ibex-vp-cosim/scripts/test_matmul_daemon.py runs 22 tests in about five seconds, each on its own temporary socket so it never disturbs a running demo daemon. Lifecycle (5): detaching, the pidfile, owner-only socket permissions, SIGTERM cleanup, refusing a second daemon, replacing a stale socket, never deleting a regular file. Protocol (6): GEMM results for N = 1 to 64 against a Python reference with full-range int32 values and wrap-around, requests sent a few bytes at a time, every error code, and which errors keep or close the connection. Parallel (1): six clients at once. End to end (3): the firmware passes through the daemon; QEMU refuses to start without a daemon; the firmware fails cleanly without the plugin. Recovery (2): the daemon restarted while QEMU is paused, and a fake daemon that never answers. Baseline (2): the direct build gives the same checksums, and the timing summary works. GDB (1): a scripted debugging session. Scripts (2): the launcher and the control script.

## Slide 19: Same results on two platforms
macOS
Apple M3 Pro, arm64
Host compiler: Clang
RISC-V: xPack GCC 15
ISA: rv32imc_zicsr_zifencei
Linux
HP ENVY 17, x86-64
Host compiler: GCC
RISC-V: older GCC
ISA: rv32imc
Checksums
4×4 FFFE8FC9
8×8 FFFFE360
16×16 FFFE87A3
32×32 001F11EC
identical on both
Different hosts, compilers, and toolchains: results match bit for bit.
Notes: The same code was built and run on two very different machines. The Mac is Apple Silicon (arm64) with Clang as the host compiler and the xPack RISC-V GCC 15, which needs the newer rv32imc_zicsr_zifencei ISA name. The Linux laptop is x86-64 with GCC as the host compiler and an older RISC-V GCC that only understands plain rv32imc; the Makefile's toolchain probe picked the right name automatically after the first Linux build failed. On both, the four result checksums printed by the firmware are identical, which shows the NPU results are bit-exact across hosts and compilers. The math uses unsigned 32-bit arithmetic on purpose, so overflow wraps exactly like the RV32 guest's own calculation.

## Slide 20: Lessons and next steps
04
What broke, how to run it, where to go next
Notes: This last section covers the problems we hit and how they were fixed, the commands to run everything, the current limits, and the natural next steps.

## Slide 21: Problems found and fixed
QEMU had no plugin support
Reconfigured in place with config.status --enable-plugins, keeping every option.
QEMU froze if the daemon stalled
A test caught it. Fix: non-blocking socket, deadlines on every send.
Pidfile could name a reused PID
stop now asks the daemon for its PID over the socket.
Linux build: unknown “zifencei”
The Makefile now probes the toolchain for its ISA naming.
macOS timings showed 0 ns
Switched to a nanosecond clock (CLOCK_UPTIME_RAW).
Expected speedup didn't hold
Measured against a direct baseline and documented the real numbers.
Notes: Six problems shaped the final design. 1: QEMU on the Mac had been built without plugin support; we re-ran its configure through config.status with --enable-plugins, so every existing option and machine was kept. 2: the most important one: a test with a fake daemon that never answers made QEMU freeze. A 32x32 request is about 8 KB, which fills macOS's Unix socket buffer, and send() blocked forever because the timeout only covered the reply. A stack sample showed the vCPU stuck in sendto, and a small probe program proved macOS ignores MSG_DONTWAIT on Unix stream sockets. Fix: an O_NONBLOCK socket with every send under the same deadline. 3: the first stop command trusted the pidfile, which could name a reused PID; it now asks the daemon. 4: the Linux laptop's older RISC-V GCC rejected the 'zifencei' ISA name; the Makefile now probes the toolchain. 5: macOS's CLOCK_MONOTONIC only has microsecond resolution, so timings showed 0 ns; we switched to CLOCK_UPTIME_RAW. 6: the expectation that a daemon would be faster than the direct implementation didn't hold up; we built a fair baseline, measured, and documented the real numbers.

## Slide 22: How to run it
# in every new terminal
cd ~/Ibex_verilator
source ./env.sh
# one command: daemon + VP
./ibex-vp-cosim/run_matmul_plugin.sh
# two terminals: live daemon, then VP runs
./ibex-vp-cosim/matmul_daemon.sh foreground
./ibex-vp-cosim/run_matmul_plugin.sh
# debug: VP waits for GDB on port 1234
./ibex-vp-cosim/run_matmul_plugin.sh --gdb
# tests and benchmark
python3 ibex-vp-cosim/scripts/test_matmul_daemon.py
python3 ibex-vp-cosim/scripts/bench_npu.py
What you'll see
Four checksums, a rejected request, the daemon's log, then Result: PASS.
Attach GDB
In terminal B, run
riscv32-unknown-elf-gdb
on the firmware ELF, then target remote :1234.
Notes: Everything runs from the repository folder; in every new terminal, cd into it and source env.sh. The one-command demo builds what changed, starts a daemon if none is running, runs the VP, prints the daemon's log for the run, and stops the daemon it started; it ends with 'Result: PASS'. To see the NPU as a separate service, run matmul_daemon.sh foreground in one terminal and the demo as often as you like in another; the daemon's request total keeps growing. For debugging, run the demo with --gdb and attach GDB from a second terminal. The test suite takes about five seconds; the benchmark about a minute. Setup from an empty machine is in the README.

## Slide 23: Limits and next steps
Today
Functional only: no NPU timing model
Synchronous: the VP waits for every request
Guest addresses treated as physical (no MMU)
Same machine only (Unix socket)
Next
Asynchronous requests, so the guest and NPU overlap
A Verilator RTL NPU behind the same protocol
A faster kernel on Linux (-O3, vectorized)
Shared memory or TCP for bigger or remote NPUs
Notes: Today's limits: the NPU is a functional model, so results are exact but no accelerator timing is modeled and guest time doesn't advance for NPU work. Requests are synchronous, which is what keeps runs deterministic but also why the daemon can't beat the direct build on speed. The plugin passes guest addresses straight to QEMU's memory API, which is right for this M-mode firmware with no MMU; firmware that enables address translation would need the plugin to translate first. The Unix socket limits it to one machine. Next steps, roughly in order of value: asynchronous requests so the guest computes while the NPU works on another core, which is where a daemon can actually win on speed; a Verilator RTL NPU behind the same wire protocol, the strongest reason for the process split; building the daemon's kernel with -O3 on Linux, where GCC at -O2 likely doesn't vectorize it; and shared memory or TCP for large matrices or a remote NPU.

## Slide 24: Key takeaways
1
The NPU is its own process, connected to QEMU by a TCG plugin, with no QEMU patch.
2
The guest waits at the doorbell, so results are deterministic and exact to the bit.
3
I/O performance and GDB are unchanged; each daemon request adds 11–21 µs.
4
22 tests and two platforms back every claim in this deck.
Read more: README.md · docs/MATMUL_DAEMON.md · docs/MATMUL_DEEP_DIVE.md
Notes: Four things to remember. The NPU runs as its own process and a TCG plugin connects it to QEMU, so QEMU's source never changed. The guest waits at the doorbell, so every run is deterministic and the results are bit-exact on every platform. Guest I/O performance and GDB debugging are unchanged by the NPU; the price of the process split is 11 to 21 µs per request. And every claim here is backed by the 22 automated tests and by runs on both macOS and Linux. For details: the README for setup and use, docs/MATMUL_DAEMON.md for the protocol, and docs/MATMUL_DEEP_DIVE.md for a code walkthrough with line references.